## Slide 1: Topic 1: Fundamentals of Logical Algebra
CST205 Digital Logic

## Slide 2: Topic Outlines
Number Systems, Binary Code
Axiom of Logical Algebra
Minterm, Maxterm
Simplification of logic functions

## Slide 3: Number Systems
Numbering systems are used by digital computers for computation.
Important numbering systems are:
  Decimal system (base-10)
  Binary system (base-2)
  Hexadecimal system (base-16)
  Octal system (base-8)

## Slide 4: Common Number Systems
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 5: Decimal Number System
Base (also called radix) = 10
  10 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Digit Position
  Integer & fraction
Digit Weight
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
5
1
2
7
4
10
1
0.1
100
0.01
500
10
2
0.7
0.04
d2*B2+d1*B1+d0*B0+d-1*B-1+d-2*B-2
(512.74)10

## Slide 6: Binary Number System
Base = 2
  2 digits { 0, 1 }, called binary digits or “bits”
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Bit x Weight”
Formal Notation
Groups of bits 4 bits = Nibble
8 bits = Byte
1
0
-1
2
-2
2
1
1/2
4
1/4
1
0
1
0
1
1 *22+0 *21+1 *20+0 *2-1+1 *2-2
=(5.25)10
(101.01)2
1 0 1 1
1 1 0 0 0 1 0 1

## Slide 7: Octal Number System
Base = 8
  8 digits { 0, 1, 2, 3, 4, 5, 6, 7 }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
8
1
1/8
64
1/64
5
1
2
7
4
5 *82+1 *81+2 *80+7 *8-1+4 *8-2
=(330.9375)10
(512.74)8

## Slide 8: Hexadecimal Number System
Base = 16
  16 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
16
1
1/16
256
1/256
1
E
5
7
A
1 *162+14 *161+5 *160+7 *16-1+10 *16-2
=(485.4765625)10
(1E5.7A)16

## Slide 9: Binary System
The binary system represents numbers in only two digit, 0 and 1.
The binary system is a base-2 system.
The position of 0 or 1 in a binary number indicates its weights, or value within the number.
The weights in a binary number are based on the powers of 2.

## Slide 11: Binary Weights
The weight structure of binary number is
Positive Powers of 2 (Whole numbers) |  |  |  |  |  |  |  |  | Negative Powers of 2 (Fractional Number) |  |  |  |  | 
28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6
256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 1 2 | 1 4 | 1 8 | 1 16 | 1 32 | 1 64

## Slide 12: Conversion Among Bases
The possibilities:
Hexadecimal
Decimal
Octal
Binary

## Slide 13: Conversion of binary number to decimal number
Convert the binary number 1101101 to decimal.
Solution:
Weight:
Binary number:
1101101=(261)+(251)+(240)+(231)+(221)+(210)+(201)
= 64 + 32 + 0 + 8 + 4 + 0 + 1
= 109.

## Slide 14: Example
Convert the binary number 10010001 to decimal.
Solution:

## Slide 15: Another example with fractional binary number
Convert the fractional binary number 0.1011 to decimal.
Solution:
Weight: 21 22 23 24
Binary number: 0 . 1 0 1 1
0.1011 = (21) + (220) + (231) + (241)
= 0.5 + 0 + 0.125 + 0.0625
= 0.6875

## Slide 16: Conversion of decimal number to binary number
Convert the following decimal numbers to binary:
(a) 19 (b) 45

## Slide 17: Solutions
(a) 19 = 100112
(b) 45 = 1011012

## Slide 18: Convert decimal to fractional binary number
Convert decimal 0.3125 to binary.
Answer: 0.3125 = 0.01012.
Method: Repeated multiplication by 2 as follows:

## Slide 19: Addition in binary system
The 4 basic rules of adding binary digits (or bits) are:
For example, add binary 11 to binary 1:

## Slide 20: More addition examples
Add the following binary numbers:
(a) 11+11 (b) 100+10 (c) 111+11 (d) 110+100
Solutions:

## Slide 21: Binary subtraction
The 4 basic rules for subtracting bits are:
0 0 = 0
1  = 0
1 0 = 1
10 1 = 1

## Slide 22: Example of binary subtraction
Perform the following binary subtraction:
(a) 11  01 (b) 11  10
Solution:

## Slide 23: Binary multiplication
The 4 basic rules for multiplying bits are:
0 0 = 0
0 1 = 0
1 0 = 0
1 1 = 1

## Slide 24: Example of binary multiplication
Perform the following binary multiplications:
(a) 11 11 (b) 101  111
Solution:

## Slide 25: Binary division
Perform the following binary division:
(a) 110  11 (b) 110  10
Solution:

## Slide 26: Hexadecimal system
The hexadecimal number system has a base 16. It is composed of 16 numeric (0-9) and alphabetic characters (A-F).

## Slide 27: Binary to Hex Conversion
Convert the following binary numbers to hexadecimal:
(a) 1100101001010111 (b) 111111000101101001
Solution:

## Slide 28: Hex to Binary Conversion
Determine the binary numbers for the following hexadecimal numbers:
(a) 10A416 (b) CF8E16 (c) 974216
Solution:

## Slide 29: Octal System
The octal system is base-8. It is composed of 8 digits, which are:
0, 1, 2, 3, 4, 5, 6, 7
To count above 7, begin another column and start over:
10, 11, 12, 13, 14, 15, 16, 17, 20, 21, ...

## Slide 30: Octal to Binary Conversion
Because each octal digit can be represented by a 3-bit binary number, it is very easy to convert from octal to binary.
Each octal digit is represented by 3 bits as shown in table below.
Octal Digit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Binary | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111

## Slide 31: Example of octal to binary conversion
Convert each of the following octal number to binary:
(a) 138 (b) 258 (c) 1408 (d) 75268
Solutions:

## Slide 32: Binary to Octal Conversion
Convert each of the following binary numbers to octal:
(a) 110101 (b) 101111001 (c) 100110011010
(d) 11010000100
Solutions:

## Slide 33: Octal − Hexadecimal Conversion
Convert to Binary/Decimal as an intermediate step
Example:
( 0 1 0 1 1 0 . 0 1 0 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Octal to Hex & Hex to Octal)
( 2 6 . 2 )8
Assume Zeros

## Slide 34: Signed Numbers
A signed binary number consists of both sign and magnitude information.
The sign indicates whether a number is positive or negative, and the magnitude is the value of the number.
There are 3 forms in which signed integer numbers can be represented in binary:
Sign-magnitude
1’s complement (the first complement)
2’s complement (the second complement)

## Slide 35: Sign-Magnitude Form
The left most bit is the sign bit and the remaining bits are the magnitude bit.
A negative number has the same magnitude bits as the corresponding postive number but the sign bit is a 1 rather than a 0.
For example, +25 in sign-magnitude form is:
While 25 in sign magnitude form is:
10011001

## Slide 36: 1s Complement
Positive numbers in 1’s complement form are represented the same way as the positive sign-magnitude form.
Negative numbers are the complements of the corresponding bits of the positive numbers.
For example, using 8-bits, the decimal number 25 is expressed as complement of all bits in +25 = 00011001 as
11100110

## Slide 37: 2s Complement
Positive numbers in 2’s complement form are represented the same way as in the sign-magnitude and 1’s complement forms.
Negative numbers are the converted by first inverting the bits in the corresponding positive numbers, then add 1 to the inverted bits.
For example, 25 is converted to 2’s complement is:
+25 = 00011001 inverted to 11100110, then add 1 to become 11100111

## Slide 38: Example of signed number representations
Express the decimal number 39 as an 8-bit sign magnitude, 1’s complement and 2’s complement forms.
Solution:
+39 = 00100111
Sign-magnitude: 10100111
1’s complement: 11011000
2’s complement: 11011001

## Slide 39: 2s Complement

## Slide 40
Any Questions