## Slide 1: Topic 1: Fundamentals of Logical Algebra
CST205 Digital Logic

## Slide 2: Product term
In the last example, each input combination that produces output 1 can be represented in the form of variable terms 1011  A B’ C D
1100 A B C’ D’
1101 A B C’ D
1110 A B C D’
1111 A B C D
We can expand the logic equation
Z = A ( B + CD) = A B’ C D + A B C’ D’ + A B C’ D + A B C D’
+ A B C D
The right hand side is the sum of product (SOP) of the logic equation.
Each term is called a product term. For example, AB’CD is one product term.

## Slide 3: Simplifications of logic functions
A logic expression can be reduced to its simplest form using the laws and theorems of Boolean algebra we have learned so far.
For example , simplify the Boolean expression
AB + A(B + C) + B(B + C)

## Slide 4: Solution
AB + A(B + C) + B(B + C)
= AB + AB + AC + BB + BC
= AB + AC + B + BC
= AB + AC + B(1 + C)
= AB + AC + B · 1
= AB + AC + B
= AB + B + AC
= (A + 1) B + AC
= 1·B + AC
= B + AC
[B.B=B]
[AB+AB=AB]
[1+B=1]
[1.B=B]
[1+B=1]
[1.B=B]

## Slide 5: Solution (Continued)
Simplification of Boolean expression results in fewer gates for the same function.

## Slide 6: More examples
Simplify the following Boolean expressions:
AB’ + A(B+C)’ + B(B+C)’
[AB’(C + BD) + A’B’]C
A’BC + AB’C’ + A’B’C’ + AB’C + ABC

## Slide 7: The Sum of Products (SOP)
The Boolean expressions in the previous slide examples are written in the form called the sum of products.
When two or more product terms are summed by Boolean addition, the resulting expression is a sum-of-products (SOP).
For example, AB + ABC
ABC + CDE + B’CD’
are all sum of products (SOP).

## Slide 8: Example of SOPs
Convert each of the following Boolean expressions to SOP form:
(a) AB + B(CD+EF) (b) (A+B)(B+C+D) (c) [(A+B)’+C]’
Answers:
(a) AB + BCD + BEF
(b) AB + AC + AD + B + BC + BD
(c) AC’ + BC’

## Slide 9: The standard SOP
A standard SOP expression is one in which all the variables in the domain appear in each product term in the expression.
For example, AB’CD+A’B’CD’+ABC’D’ is a standard SOP expression.
But A’BC’ + AB’D + A’BC’D is NOT a standard SOP form because the first product term is missing the D or D’ variable and the second product term is missing the C or C’ variable.

## Slide 10: The Product of Sum (POS)
When two or more sum terms are multiplied, the resulting expression is a product-of-sums (POS).
For example, (A’ + B)(A + B ‘ + C)
(A’ + B’ + C’)(C + D’ + E)(B’ + C + D)
A’(A + B’ + C)(B’ + C’ +D)
Note that (A + B + C)’ is not a POS because in a POS a single overbar cannot extend over more than one variable.

## Slide 11: The Standard POS
A standard POS expression is one in which all the variables in the domain appear in each sum term in the expression.
For example, (A’+B’+C’+D’)(A+B’+C+D)(A+B+C’+D) is a standard POS expression.
But (A+B’+C)(A+B+D’)(A+B’+C’+D) is not a standard POS form because the first sum term is missing a D or D’ variable and the second sum term is missing the C or C’ variable.

## Slide 12: Converting standard SOP to standard POS
The binary value of the product terms in a given standard SOP expression are not present in the equivalent standard POS expression.
Also, the binary values that are not present in the SOP expression are present in the equivalent POS expression.
To convert from standard SOP to standard POS see example in the next slide.

## Slide 13: Example
Convert the following SOP expression to an equivalent POS expression.
A’B’C’ + A’BC’ + A’BC + AB’C + ABC
Solution:
Write the binary numbers represented by each product term above.
000 + 010 + 011 + 101 + 111
Write the binary numbers not present in the list above. 001, 100, 110
Write the POS expression by converting the binary numbers above into product of sum terms.
(A + B + C’)(A’ + B + C)(A’ + B’ + C)

## Slide 14: Converting SOP expressions to truth table format
Develop a truth table for the standard SOP expression A’B’C + AB’C’ + ABC.
A | B | C | Z | Product Term
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | A’B’C
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | AB’C’
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 0 | 
1 | 1 | 1 | 1 | ABC

## Slide 15: Converting POS expressions to truth table format
Develop a truth table for the standard POS expression (A+B+C)(A+B’+C)(A+B’+C’)(A’+B+C’)(A’+B’+C).
A | B | C | Z | Sum Term
0 | 0 | 0 | 0 | (A+B+C)
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | (A+B’+C)
0 | 1 | 1 | 0 | (A+B’+C’)
1 | 0 | 0 | 1 | 
1 | 0 | 1 | 0 | (A’+B+C’)
1 | 1 | 0 | 0 | (A’+B’+C)
1 | 1 | 1 | 1 | 

## Slide 16: Determining standard expressions from a truth table
SOP expression: Z = A’BC + AB’C’ + ABC’ + ABC
POS expression: Z = (A+B+C)(A+B+C’)(A+B’+C)(A’+B+C’)
A | B | C | Z | Sum/Product Term
0 | 0 | 0 | 0 | (A+B+C)
0 | 0 | 1 | 0 | (A+B+C’)
0 | 1 | 0 | 0 | (A+B’+C)
0 | 1 | 1 | 1 | A’BC
1 | 0 | 0 | 1 | AB’C’
1 | 0 | 1 | 0 | (A’+B+C’)
1 | 1 | 0 | 1 | ABC’
1 | 1 | 1 | 1 | ABC

## Slide 17: Canonical Forms
A function with n variables is in canonical form if the SOP or POS expression has all the n variables (or their complements) appearing exactly once in each term.
For example,
f1(A,B,C) = A’BC’+ABC’+A’BC+ABC (canonical SOP)
f2(A,B,C) = (A+B+C)(A+B+C’)(A’+B+C) (canonical POS)
But
f3(A,B,C) = A’B+ABC’+B (not in canonical form)

## Slide 18: Minterm
A minterm of n variables is a product of the variables in which each appears exactly once in true or complemented form.
For example, minterms of 2 variables A and B are:
A’ B’ (representing 00)
A’ B (representing 01)
A B’ (representing 10)
A B (representing 11)
An n-variable minterm is a normal product terms with n literals. There are 2n such product terms.

## Slide 19: Writing canonical form in SOP expression
Each SOP product term has its own minterm and minterm number as shown in table below.

## Slide 20: Example
Write the canonical form of the following equation in terms of the sum of its minterm numbers.
f1(A, B, C) = A’BC’ + A’BC + ABC’
Solution:
f1(A,B,C) = m2 + m3 +m6
or
f1(A,B,C) = ∑m(2, 3, 6)
Note: The order of the variables in the functional notation f(A,B,C) is important. For example,
f1(A,B,C) = ∑ m(2,3,6) (A is the MSB, C is the LSB)
f1(C,B,A) = ∑ m(2,3,6) (C is the MSB, A is the LSB)

## Slide 21: Maxterm
A maxterm of n variables is a sum of the variables in which each appears exactly once in true or complemented form.
For example, maxterms of 2 variables A and B are:
A + B (representing 0 + 0)
A + B’ (representing 0 + 1)
A’ + B (representing 1 + 0)
A’ + B’ (representing 1 + 1)
An n-variable maxterm is a normal sum terms with n literals. There are 2n such sum terms.

## Slide 22: Writing canonical form in POS expression
Each POS sum term has its own maxterm and maxterm number as shown in table below.

## Slide 23: Example
Write the canonical form of the following equation in terms of the sum of its maxterm numbers.
fx(A,B,C) = (A’+B+C)(A+B+C’)(A+B+C)
Solution:
fx(A,B,C) = M4M1M0
Or
fx(A,B,C) = ∏M(4,1,0)

## Slide 24: Comparison between minterm and maxterm
A minterm can be defined as a product term that is 1
in exactly one row of the truth table.
A maxterm can be defined as a sum term that is 0
in exactly one row of the truth table.
X | Y | Z | Minterm | Maxterm
0 | 0 | 0 | X’Y’Z’ | X + Y + Z
0 | 0 | 1 | X’Y’Z | X + Y + Z’
0 | 1 | 0 | X’YZ’ | X + Y’ + Z
0 | 1 | 1 | X’YZ | X + Y’ + Z’
1 | 0 | 0 | XY’Z’ | X’ + Y + Z
1 | 0 | 1 | XY’Z | X’ + Y + Z’
1 | 1 | 0 | XYZ’ | X’ + Y’ + Z
1 | 1 | 1 | XYZ | X’ + Y’ + Z’

## Slide 25: Don’t care conditions
A function may be incompletely specified. This function has don’t care terms.
Don’t care arises when:
  The function has certain input combinations that can never occur. If that is the case, we don’t care what the output is for those inputs.
  All input combinations of a function occur but we don’t care whether the output is 1 or 0 for certain input combinations.

## Slide 26: Don’t care conditions
Don’t care terms are included in logic design (assign a 1 to it) if they help to simplify the logic circuit or otherwise omitted (assign a 0 to it).
For example, the truth table below shows an incompletely specified function. Don’t care is represented by ‘X’.

## Slide 27: Canonical form with don’t care conditions
Example: Write down the SOP expression and POS expression in canonical forms. Don’t care is indicated by X.
F(A,B,C) = ∑m(0,3,7) + ∑ d(1,6)
F(A,B,C) = ∏M(2,4,5)· ∏ D(1,6)

## Slide 28: Don’t Care Example
F(A,B,C) = ∑m(0,3,7) + ∑ d(1,6)
F(A,B,C) = ∏M(2,4,5)· ∏ D(1,6)
Note that we can assign 0 or 1 to the don’t care output, X and still obtain the required outputs.
If we assign 0 to both X, we get
F = A’B’C’ + A’BC + ABC = A’B’C’ + BC
If we assign 1 to the first X and 0 to the second, we get
F = A’B’C’ + A’B’C + A’BC + ABC = A’B’ + BC
If we assign 1 to both X, we get F = A’B’ + BC + AB.
The assignment that will produce the simplest functions are preferred.

## Slide 29: Universal Gates: NAND and NOR
AND/OR/NOT gates are sufficient for building any Boolean functions.
However, other gates are also used because:
(i) usefulness
(ii) economical on transistors
(iii) self-sufficient
NAND/NOR: economical, self-sufficient
XOR: useful (e.g. parity bit generation)

## Slide 30: NAND Gate
NAND gate is self-sufficient (can build any logic circuit with it).
Can be used to implement AND/OR/NOT.
Implementing an inverter using NAND gate:
(x.x)' = x' (T1: idempotency)
x
x'

## Slide 31: NAND Gate
((x.y)‘.(x.y)')' = ((x.y)')' idempotency
= (x.y) involution
((x.x)‘.(y.y)')' = (x'y')' idempotency
= x''+y'' DeMorgan
= x+y involution
Implementing AND using NAND gates:
Implementing OR using NAND gates:
x
x.y
y
(x.y)'
x
x+y
y
x'
y'

## Slide 32: NOR Gate
NOR gate is also self-sufficient.
Can be used to implement AND/OR/NOT.
Implementing an inverter using NOR gate:
(x+x)' = x' (T1: idempotency)
x
x'

## Slide 33: NOR Gate
((x+x)'+(y+y)')'=(x'+y')' idempotency
= x''.y'' DeMorgan
= x.y involution
((x+y)'+(x+y)')' = ((x+y)')' idempotency
= (x+y) involution
Implementing AND using NOR gates:
Implementing OR using NOR gates:
x
x+y
y
(x+y)'
x
x.y
y
x'
y'

## Slide 34: Implementation using NAND gates
Possible to implement any Boolean expression using NAND gates.
Procedure:
(i) Obtain Boolean expression:
e.g. F3 = xy'+x'z
(ii) Use DeMorgan theorem to obtain expression using 2-level NAND gates
e.g. F3 = xy'+x'z
= (xy'+x'z) ' ' by involution
= ((xy')' . (x'z)')' DeMorgan

## Slide 35: Implementation using NAND gates (contd..)
F3 = ((xy')'.(x'z)') ' = xy' + x'z
x'
z
F3 = ((xy')'.(x'z)')'
= xy' + x'z
(x'z)'
(xy')'
x
y'

## Slide 36: Implementation using NOR gates
F6 = xy'+x'z
= (x’+y)’ + (x+z’)’ DeMorgan
x
z'
F6
(x+z’)'
(x’+y)'
x'
y
((x’+y)’ + (x+z’)’)’
(x’+y)’ + (x+z’)’
=xy’+x’z

## Slide 37
Any Questions