## Slide 1: Tutorial 4

## Slide 2
Question 1: An air-conditioner in an office will be turned on if on working days, the temperature rises above 28C or the relative humidity rises above 90% during office hours, or if the relative humidity rises above 90% after office hour. On working days, the air-conditioner will be turned on if at any time, both the temperature goes above 28C and the relative humidity goes above 90%. During holidays, the air-conditioner can only be turned on with a switch.
Let W = working days, H = office hours, T = temperature above 28C,
R = relative humidity above 90%, S = switch on, A = air-conditioner on.
Write an expression relating A with the input variables. Simplify it and implement it with AND, OR and NOT gates.
Question 2: A bank vault has three locks with different keys for each lock. Each lock is held by a different person and in order to open the vault, at least two persons must insert their keys into the locks. Let A, B and C signifies that a key is inserted in lock 1, 2 and 3 respectively. Let Z = 1 if the door should open.
(a) Find the minterm and maxterm expansions for Z
(b) Use a K-map to simplify the function.
(c) Implement the function using logic gates.
Question 2: Implement the logic circuit:

## Slide 3
Question 3: Given that f(a,b,c,d)=∑m(0,1,3,5,6,7,8,10,14,15),
(a) Draw the Karnaugh map and loop all the prime implicants.
(b) Find all the essential prime implicants
(c) Write the minimum SOP expression for f.
Note: An implicant of a function F is any single 1 or a group of 1’s which can be combined together on a K-map of F to represent a product term.
A prime implicant is an implicant which cannot be combined with another term to eliminate a variable.
If a minterm is covered by only one prime implicant, that prime implicant is said to be an essential prime implicant.
Question 4: Find the minimum SOP and minimum POS for the following using K-maps.
(a) f(a,b,c,d) = ∏M(0,1,6,8,11,12)·∏D(3,7,14,15)
(b) f(a,b,c,d) =∑m(1,3,4,11)+ ∑d(2,7,8,12,14,15)

## Slide 4
Question 5: Given that F = AB’D’ + A’B + A’C + CD.
(a) Find the maxterm expansion for F.
(b) Use K-map to find the minimum SOP for F’.
(c) Use K-map to find the minimum POS for F.
Question 6: Using a Karnaugh map, determine the minimum SOP expression for
F = ∑m(0,1,3,4,6,7,8,10,11,15) + ∑d(5,9)
Question 7: Given f = a’c + bc’d + ac’d, find a minimum two-level circuit implementation of f using
(a) AND and OR gates
(b) NAND gates alone
(c) NOR gates alone
Assume inputs are available in both complemented and uncomplemented forms.

## Slide 5
Question 8: Minimize f(a,b,c,d) = ∑m(0,1,5,7,8,9,12,14,15) + ∑d(3,11,13) using Karnaugh map. Then design both NAND and NOR implementations.
Assume inputs are available in both complemented and uncomplemented forms.
Question 9: Find a minimum three-level NOR gate circuit to implement
f = a’b’+abd+acd.
Question 10: Design a minimum two-level, multiple-output AND-OR circuit to realize these functions
F1(a,b,c,d) = ∑m(2,3,5,6,7,8,10)
F2(a,b,c,d) = ∑m(0,1,2,3,4,5,7,8,10)